## Slide 1: UniPhier Audio Subsystem Overview
June 12 2017
Socionext Inc.
Katsuhiro Suzuki

## Slide 2: Agenda
Overview
Port
RB (Ring Buffer)
DMA
PB (DMA interface for Port)
Usecases

## Slide 3: Overview
SoC
UniPhier Audio Subsystem (AIO)
  Receive digital audio signal (ex. I2S, IEC, ...) from other LSI or other core in UniPhier
  Send digital audio signal to others
  Convert audio signal to audio data (ex. LPCM)
  Store audio data to main memory for CPU, DSP, ...
Other Core
AIO
Other Core
Other LSI
Other LSI
I2S,
IEC,
...
I2S,
IEC,
...
Mem
LPCM

## Slide 4: Port: Overview
SoC
In/Out digital audio signal (I2S, IEC) from/to outer of Audio Subsystem (AIO)
  Physical port: data in/out outer world via SoC pins
  Virtual port: interconnect AIO and other cores
  But SW need not care about Physical or Virtual
Convert signal <-> audio data (ex. LPCM)
Other Core
AIO
Other Core
OPort
OPort
IPort
IPort
Other LSI
Other LSI
I2S,
IEC,
...
I2S,
IEC,
...

## Slide 5: Port: Physical or Virtual
What SoC pin/core is connected to port?
  It depends SoC implementation
LD20 Port | Signal | Type | Core | Pin
PCMIN1 | 2ch I2S | Both | HDMI | AI1Dx
PCMIN2 | 2ch I2S | Both | SIF | AI2Dx
PCMIN3 | 2ch I2S | Virt | EVEA | -
IECIN1 | IEC | Both | HDMI | AI1IEC
HPCMOUT1 | 8ch I2S | Phys | - | AO1Dx
PCMOUT1 | 8ch I2S | Phys | - | AO2Dx
PCMOUT2 | 2ch I2S | Virt | EVEA | -
PCMOUT3 | 2ch I2S | Virt | EVEA | -
HIECOUT1 | IEC | Phys | - | AO1IEC
IECOUT1 | IEC | Phys | - | AO1ARC
IPort
for
capture
OPort
for
playback

## Slide 6: RB: Overview
Ring buffer on Main memory
  begin, end of buffer address (physical address)
  read address and write address of AIO's DMA
CPU can read/write contents of buffer directly

## Slide 7: DMA: Overview
2 types of AIO DMA
  for playback: RB to PBout
  for capture: PBin to RB
Transfer modes
  Cyclic: transfer all audio data on RB and loop to begin of RB, non stop
  Simple: transfer single chunk specified and stop the DMA
DMA has Input/Output selectors
PBin
DMA
Port
DMA
RB
DMA
RB
RB
DMA
PBout
RB

## Slide 8: DMA: input/output selectors
Every DMA has own PB
RB is NOT bounded by DMA
Registers
  Out: CDA2D_DSTAMODE[rssel]
  In: CDA2D_SRCAMODE[rssel]
LD20 DMA | PB channel
ch0 | PBout0
ch1 | PBout1
ch2 | PBout2
ch3 | PBout3
ch5 | PBout5
ch6 | PBout6
ch7 | PBout7
ch8 | PBout8
ch12 | PBout12
ch16 | PBin0
ch17 | PBin1
ch18 | PBin2
ch22 | PBin6
ch23 | PBin7
ch26 | PBin10
ch27 | PBin11
PBout
DMA
16 ... 27
RB
SRC
rssel
DMA
ch1
RB
DMA
0 ... 12
RB
RB
selctor(in)
PBin
DST
rssel
DMA
ch17
RB
RB
selctor(out)
for
playback
for
capture

## Slide 9: PB: Overview
A bridge of AIO DMA and Port
  AIO's DMA can transport audio data to PB or RB
  DMA cannot send/receive audio data to Port directly
PBin has input selector
PBout has no output selector (use OPort input selector)
OPort
PBout
PBin
IPort
Other LSI
Other LSI
DMA
DMA
LPCM
I2S
LPCM
I2S
LPCM
LPCM

## Slide 10: PB, Port: input/output selectors
aoutsel
SW can connect PB and Port as you like
Registers
  PBin, IPort: A2SWPBinMXCtr[pbinsel]
  PBout, OPort: A2SWOPortMXPath[aoutsel]
PBout1
OPort1
PBout2
IPort1
OPort
PBout
Other LSI
DMA
LPCM
I2S
LPCM
pbinsel
IPort1
PBin1
IPort2
PBin
IPort
DMA
Other LSI
I2S
LPCM
LPCM

## Slide 11: Usecases
Capture
  IPort received audio signal from outer world
Playback
  OPort send audio signal to outer world
Through
  Connect IPort and OPort directly use no DMA
IPort
PBin
DMA
RB
Capture
OPort
IPort
Through
LPCM
LPCM
LPCM
RB
DMA
PBout
OPort
Playback

## Slide 12: Registers
Port
  A2SWIPortXX, A2SWOPortXX
PB
  A2SWPBinXX, A2SWPBoutXX
DMA
  CDA2D_CHXX
RB
  CDA2D_RBXX